## Slide 1
TOPIC 21
Alternating Currents
交流电
CIE 9702 · A Level Physics A2 · Paper 4
剑桥国际物理 A2 分章节讲义 · 中英双语
Notes: <!--pageType:cover-->

## Slide 2
TOPIC 21 · CIE 9702 A2 PHYSICS
Learning Outcomes
学习目标
Topic 21 Alternating Currents
02 / 13
LEARNING OUTCOMES
学习目标
By the end of this topic, you will be able to…
21.1 Characteristics of alternating currents 交流电的特征
Period, frequency, peak value and peak-to-peak value 周期/频率/峰值
Use x = x₀ sin ωt for alternating current and voltage 正弦表示
Use a CRO to measure period, frequency and peak voltage 示波器测量
21.2 Rectification and smoothing 整流与滤波
Mean power in a resistive load; r.m.s. values 平均功率与方均根值
Half-wave and full-wave (bridge) rectification 半波与桥式整流
Smoothing the rectified output using a capacitor 电容滤波
Notes: <!--pageType:content-->

## Slide 3
TOPIC 21 · CIE 9702 A2 PHYSICS
Characteristics of AC
交流电的特征
Topic 21 Alternating Currents
03 / 13
An alternating current (a.c.) periodically reverses its direction. For a sinusoidal supply, current and voltage vary with time as a sine function.
方向周期性变化的电流；正弦交流电随时间按正弦规律变化。
峰值 x₀ · 角频率 ω
• Peak value 峰值: amplitude I₀ or V₀；peak-to-peak 峰-峰值 = 2V₀
• Mean value over one cycle = 0，但传输的功率不为零 平均值零≠功率零
Chart: t →
| 0.0 | 0.131 | 0.262 | 0.393 | 0.524 | 0.654 | 0.785 | 0.916 | 1.047 | 1.178 | 1.309 | 1.44 | 1.571 | 1.702 | 1.833 | 1.963 | 2.094 | 2.225 | 2.356 | 2.487 | 2.618 | 2.749 | 2.88 | 3.011 | 3.142 | 3.272 | 3.403 | 3.534 | 3.665 | 3.796 | 3.927 | 4.058 | 4.189 | 4.32 | 4.451 | 4.581 | 4.712 | 4.843 | 4.974 | 5.105 | 5.236 | 5.367 | 5.498 | 5.629 | 5.76 | 5.89 | 6.021 | 6.152 | 6.283
V = V₀ sin ωt | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | -0.131 | -0.259 | -0.383 | -0.5 | -0.609 | -0.707 | -0.793 | -0.866 | -0.924 | -0.966 | -0.991 | -1 | -0.991 | -0.966 | -0.924 | -0.866 | -0.793 | -0.707 | -0.609 | -0.5 | -0.383 | -0.259 | -0.131 | 0
Sinusoidal a.c. voltage 正弦交流电压波形
Notes: <!--pageType:content-->

## Slide 4
TOPIC 21 · CIE 9702 A2 PHYSICS
Power in an AC Circuit
交流电路的功率
Topic 21 Alternating Currents
04 / 13
• Instantaneous power 瞬时功率: — always positive 始终为正
• Mean of sin²ωt over one cycle = ½ sin² 平均值为 1/2
• So the mean power is half the maximum power 平均功率=最大功率一半
正弦交流电专用
Chart: t →
| 0.0 | 0.131 | 0.262 | 0.393 | 0.524 | 0.654 | 0.785 | 0.916 | 1.047 | 1.178 | 1.309 | 1.44 | 1.571 | 1.702 | 1.833 | 1.963 | 2.094 | 2.225 | 2.356 | 2.487 | 2.618 | 2.749 | 2.88 | 3.011 | 3.142 | 3.272 | 3.403 | 3.534 | 3.665 | 3.796 | 3.927 | 4.058 | 4.189 | 4.32 | 4.451 | 4.581 | 4.712 | 4.843 | 4.974 | 5.105 | 5.236 | 5.367 | 5.498 | 5.629 | 5.76 | 5.89 | 6.021 | 6.152 | 6.283
i / I₀ | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | -0.131 | -0.259 | -0.383 | -0.5 | -0.609 | -0.707 | -0.793 | -0.866 | -0.924 | -0.966 | -0.991 | -1 | -0.991 | -0.966 | -0.924 | -0.866 | -0.793 | -0.707 | -0.609 | -0.5 | -0.383 | -0.259 | -0.131 | 0
p / I₀²R | 0 | 0.017 | 0.067 | 0.146 | 0.25 | 0.371 | 0.5 | 0.629 | 0.75 | 0.854 | 0.933 | 0.983 | 1 | 0.983 | 0.933 | 0.854 | 0.75 | 0.629 | 0.5 | 0.371 | 0.25 | 0.146 | 0.067 | 0.017 | 0 | 0.017 | 0.067 | 0.146 | 0.25 | 0.371 | 0.5 | 0.629 | 0.75 | 0.854 | 0.933 | 0.983 | 1 | 0.983 | 0.933 | 0.854 | 0.75 | 0.629 | 0.5 | 0.371 | 0.25 | 0.146 | 0.067 | 0.017 | 0
p is always positive; mean = ½ of peak 功率恒正，均值减半
Notes: <!--pageType:content-->

## Slide 5
TOPIC 21 · CIE 9702 A2 PHYSICS
Root-Mean-Square Values
方均根值 (r.m.s.)
Topic 21 Alternating Currents
05 / 13
The r.m.s. value of an alternating current/voltage is the value of the steady direct current/voltage that would produce thermal energy at the same rate in a resistor.
方均根值：在电阻中产生相同热效应的等效直流值。
仅适用于正弦波
• Quoted supply voltages are r.m.s. values: 230 V mains has V₀ = 325 V 市电标称值是 rms
• Power formulas use r.m.s. values:
square the values 先平方
take the mean 取平均
square root 再开方
Notes: <!--pageType:content-->

## Slide 6
TOPIC 21 · CIE 9702 A2 PHYSICS
Half-Wave Rectification
半波整流
Topic 21 Alternating Currents
06 / 13
Rectification is the conversion of a.c. into d.c. A single diode conducts only when forward-biased, so current flows through the load during only one half of each cycle.
整流=交流变直流；单个二极管正向导通、反向截止。
• Output: pulsating d.c. — one half-cycle missing 输出为脉动直流
• Diode symbol: current allowed in direction of arrow 二极管符号：箭头方向允许电流
• Simple, but wastes half of every cycle 效率低，纹波大
~
R
Chart: t →
| 0.0 | 0.131 | 0.262 | 0.393 | 0.524 | 0.654 | 0.785 | 0.916 | 1.047 | 1.178 | 1.309 | 1.44 | 1.571 | 1.702 | 1.833 | 1.963 | 2.094 | 2.225 | 2.356 | 2.487 | 2.618 | 2.749 | 2.88 | 3.011 | 3.142 | 3.272 | 3.403 | 3.534 | 3.665 | 3.796 | 3.927 | 4.058 | 4.189 | 4.32 | 4.451 | 4.581 | 4.712 | 4.843 | 4.974 | 5.105 | 5.236 | 5.367 | 5.498 | 5.629 | 5.76 | 5.89 | 6.021 | 6.152 | 6.283
input 输入 | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | -0.131 | -0.259 | -0.383 | -0.5 | -0.609 | -0.707 | -0.793 | -0.866 | -0.924 | -0.966 | -0.991 | -1 | -0.991 | -0.966 | -0.924 | -0.866 | -0.793 | -0.707 | -0.609 | -0.5 | -0.383 | -0.259 | -0.131 | 0
output 输出 | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: <!--pageType:content-->

## Slide 7
TOPIC 21 · CIE 9702 A2 PHYSICS
Full-Wave Rectification
桥式全波整流
Topic 21 Alternating Currents
07 / 13
A bridge rectifier uses four diodes. Two diodes conduct on the positive half-cycle and the other two on the negative half-cycle, so current through the load is always in the same direction.
桥式整流：四只二极管，正负半周各导通两只，负载电流方向不变。
• Output uses both half-cycles 两个半周都被利用
• Mean output double that of half-wave 平均输出是半波的两倍
• Still pulsating — needs smoothing 仍需滤波平滑
bridge of 4 diodes 四二极管电桥（菱形）
Chart: t →
| 0.0 | 0.131 | 0.262 | 0.393 | 0.524 | 0.654 | 0.785 | 0.916 | 1.047 | 1.178 | 1.309 | 1.44 | 1.571 | 1.702 | 1.833 | 1.963 | 2.094 | 2.225 | 2.356 | 2.487 | 2.618 | 2.749 | 2.88 | 3.011 | 3.142 | 3.272 | 3.403 | 3.534 | 3.665 | 3.796 | 3.927 | 4.058 | 4.189 | 4.32 | 4.451 | 4.581 | 4.712 | 4.843 | 4.974 | 5.105 | 5.236 | 5.367 | 5.498 | 5.629 | 5.76 | 5.89 | 6.021 | 6.152 | 6.283
input 输入 | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | -0.131 | -0.259 | -0.383 | -0.5 | -0.609 | -0.707 | -0.793 | -0.866 | -0.924 | -0.966 | -0.991 | -1 | -0.991 | -0.966 | -0.924 | -0.866 | -0.793 | -0.707 | -0.609 | -0.5 | -0.383 | -0.259 | -0.131 | 0
output 输出 | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0 | 0.131 | 0.259 | 0.383 | 0.5 | 0.609 | 0.707 | 0.793 | 0.866 | 0.924 | 0.966 | 0.991 | 1 | 0.991 | 0.966 | 0.924 | 0.866 | 0.793 | 0.707 | 0.609 | 0.5 | 0.383 | 0.259 | 0.131 | 0
Notes: <!--pageType:content-->

## Slide 8
TOPIC 21 · CIE 9702 A2 PHYSICS
Smoothing with a Capacitor
电容滤波
Topic 21 Alternating Currents
08 / 13
A capacitor connected in parallel with the load charges up near the peak voltage, then discharges slowly through the load when the rectified voltage falls, keeping the output nearly steady.
与负载并联的电容：峰值时充电、下降时放电补流，使输出平缓。
• Remaining small variation = ripple 残余波动称纹波
• Larger C or larger load R ⇒ slower discharge ⇒ smaller ripple C、R 越大纹波越小
• Trade-off: very large C gives large surge currents through diodes 电容太大冲击电流大
Chart: t →
Capacitor smoothing reduces ripple 滤波减小纹波
Notes: <!--pageType:content-->

## Slide 9
TOPIC 21 · CIE 9702 A2 PHYSICS
Worked Examples 21A & 21B
例题解析
Topic 21 Alternating Currents
09 / 13
WORKED EXAMPLE 21A
The variation with time t (in s) of the p.d. V (in V) of an alternating supply is
Determine: a) the peak p.d.; b) the frequency.
1. Peak value = amplitude of the sine function ⇒
2. Compare with : rad s⁻¹
3. Hz
Answer V₀ = 24 V; f = 60 Hz
WORKED EXAMPLE 21B
An a.c. signal on a CRO shows 2 complete cycles occupying 6.0 cm, with the time-base set at 0.50 ms cm⁻¹. Find the frequency.
1. Length of one cycle L = 6.0/2 = 3.0 cm
2. Period = 1.5 ms
3. Hz
Answer f ≈ 670 Hz
Notes: <!--pageType:content-->

## Slide 10
TOPIC 21 · CIE 9702 A2 PHYSICS
Worked Examples 21C & 21D
例题解析
Topic 21 Alternating Currents
10 / 13
WORKED EXAMPLE 21C
On a CRO with y-gain set at 5.0 mV cm⁻¹, the amplitude of the trace is 1.4 cm. Find the peak voltage of the signal.
1. Peak voltage = amplitude × y-gain
2. mV
Answer V₀ = 7.0 mV
WORKED EXAMPLE 21D
A 1.5 kW heater is connected to the 230 V mains. Calculate the peak current in the heater and its resistance.
1. 230 V is the r.m.s. value: A
2. Peak current A
3. Ω
Answer I₀ = 9.2 A; R = 35 Ω
Notes: <!--pageType:content-->

## Slide 11
TOPIC 21 · CIE 9702 A2 PHYSICS
Class Practice
随堂练习
Topic 21 Alternating Currents
11 / 13
Q1
The peak value of the mains voltage in India is 325 V. Calculate the r.m.s. voltage, and the mean power dissipated in a 60 Ω resistor.
Q2
A CRO trace shows one complete cycle occupying 4.0 cm with the time-base at 2.0 ms cm⁻¹. Determine the frequency of the signal.
Q3
In a bridge rectifier, state which pair of diodes conducts during the positive half-cycle of the input, and explain why the output current through the load never reverses.
Answers Q1: V_rms = 325/√2 = 230 V, P = 230²/60 ≈ 880 W Q2: T = 8.0 ms, f = 125 Hz Q3: 对角一对二极管导通；两半周电流经负载方向相同
Notes: <!--pageType:content-->

## Slide 12
TOPIC 21 · CIE 9702 A2 PHYSICS
Summary
本章小结
Topic 21 Alternating Currents
12 / 13
KEY FORMULAS 核心公式
正弦交流表示
角频率
平均功率=峰值一半
方均根电流
方均根电压
功率用 rms 值
KEY IDEAS 核心思想
• r.m.s. value = equivalent steady d.c. value giving the same heating effect 等效热效应直流值
• Half-wave: one diode, half of each cycle wasted 半波：一只二极管
• Bridge full-wave: four diodes, both half-cycles used 桥式：四只二极管
• Parallel capacitor smooths the output; ripple ↓ as C or R ↑ 并联电容滤波
Notes: <!--pageType:content-->

## Slide 13
TOPIC 21 · CIE 9702 A2 PHYSICS
Exam Tips
备考提示
Topic 21 Alternating Currents
13 / 13
I₀/√2 applies to sinusoidal waveforms only. For square or triangular waves the r.m.s. factor is different. /√2 仅适用正弦波。
Always use r.m.s. values in power calculations; using peak values overestimates power by a factor of 2. 功率计算用 rms 值。
When sketching rectified waveforms, keep the same period and amplitude as the input; for half-wave show gaps, for full-wave flip the negative half up. 画波形注意周期幅值不变。
CRO readings: period = length × time-base; peak voltage = amplitude × y-gain. Measure several cycles and average. 示波器：长度×档位。
Notes: <!--pageType:content-->