## Slide 1
TOPIC 24
Medical Physics
医学物理
CIE 9702 · A Level Physics A2 · Paper 4
剑桥国际物理 A2 分章节讲义 · 中英双语
Notes: <!--pageType:cover-->

## Slide 2
TOPIC 24 · CIE 9702 A2 PHYSICS
Learning Outcomes
学习目标
Topic 24 Medical Physics
02 / 18
LEARNING OUTCOMES
学习目标
By the end of this topic, you will be able to…
24.1 Ultrasound in medicine 医学超声
Piezo-electric effect: generating and detecting ultrasound 压电效应
Specific acoustic impedance Z = ρc and intensity reflection coefficient 声阻抗与反射系数
Attenuation I = I₀e^(−μx); A-scan and B-scan 衰减与成像方式
24.2 X-rays in medicine 医学 X 射线
Production of X-rays; minimum wavelength λmin = hc/eV X 射线产生
Attenuation mechanisms; improving image contrast 衰减与影像对比
CT scanning: image reconstruction CT 扫描
24.3 PET scanning PET 扫描
Radioactive tracers; positron emission and annihilation 示踪剂与湮灭
Detection of the two 511 keV γ-ray photons 符合探测
Notes: <!--pageType:content-->

## Slide 3
TOPIC 24 · CIE 9702 A2 PHYSICS
The Piezo-electric Effect
压电效应
Topic 24 Medical Physics
03 / 18
A piezo-electric crystal (e.g. quartz, PZT) changes shape when a p.d. is applied across it, and produces an e.m.f. across its faces when it is compressed or stretched.
压电晶体：加电压⇒形变；受形变⇒产生电动势，效应可逆。
• The effect is reversible — the same crystal generates and detects ultrasound 收发两用
• Applying an alternating p.d. makes the crystal vibrate 交变电压使晶体振动
• Vibration amplitude is greatest at the crystal's resonant frequency 共振时振幅最大
piezo-electric crystal
压电晶体
applied p.d. 加电压
deforms 形变
strain ⇒ e.m.f. 形变⇒电压
Reversible piezo-electric effect 可逆压电效应
Notes: <!--pageType:content-->

## Slide 4
TOPIC 24 · CIE 9702 A2 PHYSICS
Generating & Detecting Ultrasound
超声的产生与接收
Topic 24 Medical Physics
04 / 18
An ultrasound transducer uses a piezo-electric crystal. An alternating p.d. at the crystal's resonant frequency produces an ultrasound pulse; a returning echo makes the crystal vibrate and generates an electrical signal.
换能器：交变电压⇒超声脉冲；回波⇒电信号，同一晶体收发分时工作。
• Ultrasound = sound waves with frequency above 20 kHz; medical imaging uses 1–15 MHz 医学超声频率
• The crystal is damped to produce short pulses — transmission and reception share the same crystal 短脉冲
• Echo delay time ⇒ distance to the reflecting boundary: depth = ½ct 回波延时⇒深度
• Pulse repetition frequency limited by echo return time 脉冲重复频率受限
Notes: <!--pageType:content-->

## Slide 5
TOPIC 24 · CIE 9702 A2 PHYSICS
Ultrasound Imaging
超声成像原理
Topic 24 Medical Physics
05 / 18
• Pulses reflect at boundaries between different tissues 组织界面反射
• Echo delay ⇒ depth; echo amplitude ⇒ boundary type 延时定深度、幅度辨界面
• A-scan: 1-D graph of echo amplitude vs time 一维幅度显示
• B-scan: 2-D image built from many A-scans as the probe moves 二维图像
• Advantages: no ionising radiation, real-time, relatively cheap 无电离辐射
probe
skin 皮肤
soft tissue 软组织
bone 骨骼
pulse ↓ echo ↑
Pulse–echo principle 脉冲回波原理
Notes: <!--pageType:content-->

## Slide 6
TOPIC 24 · CIE 9702 A2 PHYSICS
Specific Acoustic Impedance
声阻抗与反射
Topic 24 Medical Physics
06 / 18
Specific acoustic impedance Z of a medium is the product of its density ρ and the speed of sound c in it (unit kg m⁻² s⁻¹).
声阻抗 Z = ρc，单位 kg m⁻² s⁻¹。
垂直入射时的强度反射系数
• Large mismatch (air↔tissue) ⇒ almost total reflection 空气界面几乎全反射
• Coupling gel excludes air so ultrasound can enter the body 耦合剂排除空气
• Bone–muscle boundary: α ≈ 0.34 — enough reflection for imaging 骨界面反射适中
• Typical Z / 10⁶ kg m⁻² s⁻¹: air ≈ 0.0004, fat 1.4, muscle 1.7, bone ≈ 6.5 典型数值
Notes: <!--pageType:content-->

## Slide 7
TOPIC 24 · CIE 9702 A2 PHYSICS
Attenuation of Ultrasound
超声的衰减
Topic 24 Medical Physics
07 / 18
As a parallel beam passes through tissue, absorption reduces its intensity exponentially. μ is the linear absorption (attenuation) coefficient of the medium.
平行束强度随深度指数衰减。
μ 取决于介质与频率
• Higher frequency ⇒ better resolution but larger μ (less penetration) 频率：分辨率↔穿透深度
• Typical μ (muscle) ≈ 0.23 cm⁻¹ at 1 MHz 典型数值
• Formula applies to a parallel beam; divergent beams also lose intensity by spreading 平行束条件
Chart: x / cm →
| 0.0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0 | 2.2 | 2.4 | 2.6 | 2.8 | 3.0 | 3.2 | 3.4 | 3.6 | 3.8 | 4.0 | 4.2 | 4.4 | 4.6 | 4.8 | 5.0 | 5.2 | 5.4 | 5.6 | 5.8 | 6.0 | 6.2 | 6.4 | 6.6 | 6.8 | 7.0 | 7.2 | 7.4 | 7.6 | 7.8 | 8.0
I / I₀ (muscle) | 1 | 0.955 | 0.912 | 0.871 | 0.832 | 0.795 | 0.759 | 0.725 | 0.692 | 0.661 | 0.631 | 0.603 | 0.576 | 0.55 | 0.525 | 0.502 | 0.479 | 0.457 | 0.437 | 0.417 | 0.399 | 0.381 | 0.363 | 0.347 | 0.332 | 0.317 | 0.302 | 0.289 | 0.276 | 0.263 | 0.252 | 0.24 | 0.229 | 0.219 | 0.209 | 0.2 | 0.191 | 0.182 | 0.174 | 0.166 | 0.159
Exponential attenuation in tissue 组织中的指数衰减
Notes: <!--pageType:content-->

## Slide 8
TOPIC 24 · CIE 9702 A2 PHYSICS
Production of X-rays
X 射线的产生
Topic 24 Medical Physics
08 / 18
X-rays are produced when high-speed electrons are suddenly decelerated by hitting a metal target (anode) in an evacuated X-ray tube.
高速电子轰击金属靶、急剧减速时产生 X 射线。
• Hot cathode emits electrons (thermionic emission) 热阴极发射电子
• High p.d. (30–150 kV) accelerates electrons to the anode 高压加速
• Only ≈ 1% of electron energy becomes X-rays — the anode needs cooling 效率低需冷却
• Rotating anode spreads the heat 旋转阳极散热
cathode 阴极
anode target 阳极靶
electron beam 电子束
X-rays
X-ray tube X 射线管
Notes: <!--pageType:content-->

## Slide 9
TOPIC 24 · CIE 9702 A2 PHYSICS
The X-ray Spectrum
X 射线谱
Topic 24 Medical Physics
09 / 18
• Continuous spectrum: bremsstrahlung — electrons decelerated in the target 连续谱（轫致辐射）
• Characteristic lines: target atoms' inner-shell transitions 特征谱线
• Sharp cut-off at the shortest wavelength 存在最短波长
• ↑ tube voltage ⇒ shorter λmin (harder X-rays); ↑ current ⇒ higher intensity 管压定硬度
全部电子动能转为一个光子
Chart: λ / 10⁻¹⁰ m →
Continuous spectrum + characteristic peaks 连续谱+特征峰
Notes: <!--pageType:content-->

## Slide 10
TOPIC 24 · CIE 9702 A2 PHYSICS
Attenuation of X-rays
X 射线的衰减与成像
Topic 24 Medical Physics
10 / 18
与超声衰减同形式
• μ depends on the medium and on photon energy μ 与介质及光子能量有关
• Bone attenuates much more than soft tissue ⇒ shadow on film 骨吸收强⇒影像对比
• X-ray image = 2-D shadow, not a lens image 影像是"影子"
• Aluminium filter removes long-wavelength photons that only add dose 铝滤片去软射线
• Contrast improved by contrast media (e.g. barium meal) 造影剂增强对比
Notes: <!--pageType:content-->

## Slide 11
TOPIC 24 · CIE 9702 A2 PHYSICS
Computed Tomography (CT)
CT 扫描
Topic 24 Medical Physics
11 / 18
In CT scanning, X-ray images of a thin slice of the body are taken from many different angles, and a computer reconstructs a detailed cross-sectional image.
多角度投影+计算机重建断层图像。
• The slice is divided into voxels; each voxel's attenuation is computed 体素重建
• Millions of calculations ⇒ powerful computer required 计算量大
• Advantage over plain X-ray: distinguishes soft tissues of similar density 软组织分辨
• 3-D image can be viewed from any angle; brightness/contrast adjustable 三维任意视角
• Disadvantage: larger radiation dose than a single X-ray 剂量较大
Notes: <!--pageType:content-->

## Slide 12
TOPIC 24 · CIE 9702 A2 PHYSICS
PET Scanning
PET 扫描原理
Topic 24 Medical Physics
12 / 18
1. Tracer with a β⁺ emitter (e.g. ¹⁸F-FDG) is injected and collects at active tissue 正电子示踪剂
2. Emitted positron annihilates with an electron 正电子与电子湮灭
3. Annihilation produces two 511 keV γ-photons travelling in opposite directions 两个反向 511 keV 光子
4. Ring detectors register photons in coincidence; the source lies on the line joining the detectors 符合探测定位
• PET maps metabolic activity, not anatomy 代谢功能成像
two 511 keV γ in opposite directions
Annihilation and coincidence detection 湮灭与符合探测
Notes: <!--pageType:content-->

## Slide 13
TOPIC 24 · CIE 9702 A2 PHYSICS
Worked Example 24A
例题解析
Topic 24 Medical Physics
13 / 18
WORKED EXAMPLE 24A
Using Z (air) = 430 kg m⁻² s⁻¹, Z (soft tissue) = 1.6 × 10⁶ kg m⁻² s⁻¹, calculate the intensity reflection coefficient for a parallel beam incident normally on: a) the air–soft tissue boundary; b) a muscle–bone boundary (Z muscle = 1.7 × 10⁶, Z bone = 6.5 × 10⁶ kg m⁻² s⁻¹).
这就是检查时必须涂耦合剂排除空气的原因。
SOLUTION 解答
Step 1
Step 2 a) α = (1.6×10⁶ − 430)² / (1.6×10⁶ + 430)² ≈ 0.999 ≈ 1.0 — almost total reflection
Step 3 b) α = (6.5 − 1.7)²/(6.5 + 1.7)² = (4.8/8.2)² = 0.34
Answer a) ≈ 1.0; b) 0.34
Notes: <!--pageType:content-->

## Slide 14
TOPIC 24 · CIE 9702 A2 PHYSICS
Worked Examples 24B & 24C
例题解析
Topic 24 Medical Physics
14 / 18
WORKED EXAMPLE 24B
Ultrasound passes through 3.5 cm of muscle, reflects at a bone surface (α = 0.34) and returns through the muscle. For muscle μ = 0.23 cm⁻¹, find the fraction of the incident intensity that arrives back.
1. Total path = 7.0 cm: I/I₀ = e^(−0.23×7.0) = 0.20
2. Reflected fraction at bone = 0.34
3. Returning fraction = 0.20 × 0.34
Answer I/I₀ = 0.068
WORKED EXAMPLE 24C
The accelerating p.d. of an X-ray tube is 30 kV. Calculate the minimum wavelength of photons in the beam. (h = 6.63×10⁻³⁴ J s, e = 1.60×10⁻¹⁹ C, c = 3.00×10⁸ m s⁻¹)
1. Maximum photon energy = electron kinetic energy: eV = hc/λmin
2. λmin = (6.63×10⁻³⁴ × 3.00×10⁸)/(1.60×10⁻¹⁹ × 30×10³)
Answer λmin = 4.1 × 10⁻¹¹ m
Notes: <!--pageType:content-->

## Slide 15
TOPIC 24 · CIE 9702 A2 PHYSICS
Worked Examples 24D & 24E
例题解析
Topic 24 Medical Physics
15 / 18
WORKED EXAMPLE 24D
The linear absorption coefficient of copper is 0.693 mm⁻¹. Calculate: a) the thickness that reduces intensity by 50%; b) the fraction transmitted through 1.2 cm of copper.
1. a) 0.50 = e^(−0.693x) ⇒ x = ln2/0.693 = 1.0 mm
2. b) I/I₀ = e^(−0.693×12) = e^(−8.3)
Answer a) 1.0 mm; b) 2.4 × 10⁻⁴
WORKED EXAMPLE 24E
Compare the image produced during an X-ray investigation with that produced in CT scanning.
1. X-ray: 2-D projection (shadow) of a 3-D object onto a flat detector
2. CT: computer-reconstructed 3-D image; sections can be viewed from many angles, with adjustable contrast
Answer 2-D shadow vs 3-D reconstruction
Notes: <!--pageType:content-->

## Slide 16
TOPIC 24 · CIE 9702 A2 PHYSICS
Class Practice
随堂练习
Topic 24 Medical Physics
16 / 18
Q1
Calculate the intensity reflection coefficient for ultrasound incident normally on a fat–muscle boundary (Z fat = 1.4 × 10⁶, Z muscle = 1.7 × 10⁶ kg m⁻² s⁻¹).
Q2
Water has μ = 0.29 cm⁻¹ for certain X-ray photons. Calculate the depth of water that reduces the intensity of a parallel beam to 3.0 × 10⁻³ of its incident value.
Q3
Put the stages of PET imaging in order and explain the role of coincidence detection: positron emission / two 511 keV photons / injection of tracer / line of response located / annihilation.
Answers Q1: (0.3/3.1)² = 9.4×10⁻³ Q2: x = ln(333)/0.29 = 20 cm Q3: 注射→正电子→湮灭→双光子→符合探测定响应线
Notes: <!--pageType:content-->

## Slide 17
TOPIC 24 · CIE 9702 A2 PHYSICS
Summary
本章小结
Topic 24 Medical Physics
17 / 18
KEY FORMULAS 核心公式
声阻抗
强度反射系数
指数衰减
X 射线最短波长
湮灭光子能量
回波测深
KEY IDEAS 核心思想
• Piezo-electric crystal both generates and detects ultrasound 压电晶体收发一体
• Coupling gel removes the air gap (α ≈ 1 at air boundary) 耦合剂排除空气
• X-ray = 2-D shadow; CT = 3-D reconstruction; PET = metabolic map 三种影像对比
• Two opposite 511 keV photons are the key to PET localisation PET 定位关键
Notes: <!--pageType:content-->

## Slide 18
TOPIC 24 · CIE 9702 A2 PHYSICS
Exam Tips
备考提示
Topic 24 Medical Physics
18 / 18
Reflection coefficient: square the difference first, then divide by the square of the sum — order matters. 先差后和的平方。
For I = I₀e^(−μx): check that μ and x have consistent units (cm⁻¹ with cm). μ 与 x 单位匹配。
Ultrasound uses pulses, not continuous waves, so that echoes can return before the next pulse is sent. 脉冲而非连续波。
PET: the two photons are simultaneous and opposite — both facts are needed for locating the source. 同时+反向缺一不可。
Notes: <!--pageType:content-->